## Slide 1: TSKS14 Multiple Antenna Communications
Lecture 1, 2020
Emil Björnson

## Slide 2: Three main benefits of multiple antenna communications
Beamforming gain
Spatial diversity
Spatial multiplexing
The course will cover all of them:
  First historical perspective
  Then the theory behind them

## Slide 3: Constructive and destructive interference
One signal:
(Normalization:
Two signals:
Power depends on the phase difference
(time delay)

## Slide 4: Omni-directional radiation
antenna
Powers spread out as a sphere
  Received power decays as 1/distance2

## Slide 5: Directive radiation – Beamforming gain
antennas
Power directed towards receiver
  Constructive interference
  Send signals with time delays
  Needs to know “direction”
Two options:
  6 times larger received power
  Use 1/6 of power to achieve same received power
Beamforming

## Slide 6: History: Beamforming
Directional communication
  E.F.W. Alexanderson, ”Transatlantic Radio Communication”, Trans. AIEE, 1919.
Directive radiation pattern
  Constructive/destructive interference patterns
  Energy savings or better performance
Called beamforming gain

## Slide 7: Multipath Propagation
Received signal:
Transmitter
Receiver
Multipath fading:
Add construtively or destructively depending on

## Slide 8: History: Spatial diversity
Diversity combining
  D.G. Brennan, “Linear diversity combining techniques,” Proc. IRE, 1959
Protect against fading/noise
  Multiple antennas with independent observations
  Small risk that multiple observations are all bad
  Improve reliability
Called diversity gain

## Slide 9: Cellular networks
Designed for mobile telephone systems
  Bullington, K. (1953). “Frequency economy in mobile radio bands”. The Bell System Technical Journal.
  Schulte, H. J. and W. A. Cornell (1960). “Multi-area mobile telephone system”. IEEE Trans. Veh. Technol.
Reuse of spectrum in space:
  Densify as usage increases
Control interference by fractional spectrum reuse, power control

## Slide 10: History: Space division multiple access (SDMA)
Multiple user communication
  S. C. Swales et al., “The Performance Enhancement of Multibeam Adaptive Base-Station Antennas for Cellular Land Mobile Radio Systems” Trans. on Vehicular Technology, 1990.
Spatial multiplexing of users
  Serve multiple users on same time and frequency
  Handle more users per base station
  Exists in 4G/5G and Wi-Fi
Called multiplexing gain

## Slide 11: History: Point-to-point multi-antenna links
Point-to-point multiple-input multiple-output (MIMO)
  G. G. Raleigh and J. M. Cioffi, “Spatio-temporal coding for wireless communications,” Globecom 1996.
Multiple streams per user
  Increase capacity (bit/s) per user
  Requires multiple paths
  Exists in 4G/5G and Wi-Fi
Also called multiplexing gain

## Slide 12: Outline of the course
Lecture 1:
  History of multiple antenna communications
  Channel capacity for single-antenna channels
Basic multi–antenna channels (Lecture 2)
Diversity and ergodic capacity (Lecture 3)
Point-to-point MIMO (Lecture 4)
Multi-user MIMO (Lectures 5-12)
  Capacity bounds, Channel estimation, Power control, etc.
Based on lecture note document:
“Introduction to Multiple Antenna Communications”
Based on the book
“Fundamentals of Massive MIMO”

## Slide 13: Example: Additive White Gaussian Noise (AWGN) Channel
Noise:
Energy per symbol:
real valued
+

## Slide 14: How to measure performance?
Data packet:
Characterized by
  How many symbols the packet contains
  How many information bits these symbols represent (determined by the modulation and coding scheme)
  Probability of incorrect decoding at the receiver
Information symbols

## Slide 15: Channel capacity
Channel capacity
  Random variables and
  Channel described by conditional distribution
Channel coding theorem
  [bit/channel use] is the capacity of the channel if: For any given and , there exist a channel coding codebook of a finite length that has rate and offers an error probability

## Slide 16: Passband and baseband signals
Bandwidth: Distance from smallest to largest frequency
0
Bandwidth (baseband):
Complex-valued signal
Described by complex samples/s
Bandwidth (passband):
Real-valued signal
Described by real samples/s
These samples are used to convey information

## Slide 17: Gaussian Distribution
is zero-mean Gaussian distributed,
  Probability density function (PDF):
Properties:

## Slide 18: Complex Gaussian Distribution
Consider independent
  is circularly symmetric complex Gaussian distributed, , with
Properties:

## Slide 19: Capacity and mutual information
Channel capacity
  Mutual information:
  Differential entropy:
  Conditional diff. entropy:
Equality if
Complex Gaussian

## Slide 20: Differential entropy of
Direct computation

## Slide 21: Capacity of complex AWGN channel
Recall:
Mutual information maximized by
Capacity:
+

## Slide 22: Point-to-point scalar channel
Continuous-time AWGN channel with channel response
  Bandwidth (Hz)
  Power (Watt)
  Noise power spectral density (Watt/Hz)
Sampling: real samples/s, complex samples/s:
  Energy per sample:
Complex Gaussian signals are capacity achieving

## Slide 23: Point-to-point scalar channel: Capacity
Sampling: real samples/s, complex samples/s:
Capacity:
  Depends on and

## Slide 24: Capacity behaviors
Power limited region
Bandwidth
limited
region
Assumption: Hz
SNR:
  Linear for small SNR
  Almost flat for large SNR

## Slide 25: Summary
Capacity of point-to-point channel:
SNR per degree of freedom (symbol):
Behaviors
  Low SNR: grows linearly with power
  High SNR: grows linearly with bandwidth

## Slide 26
End of Lecture 1
TSKS14 Multiple Antenna Communications